## Slide 1: Partition-based scheduling
Multicore Systems

## Slide 2: Motivation
Mixed Criticality Systems: Some tasks more critical than others [1].
Periodic Tasks: Consist of infinite sequence of identical instances activated at a constant rate [2].
Increasing computational demand.
Advances in integrated circuit miniaturization.
Solution: Multicore systems.
Categorization of multi-core processors:
  Homogeneous Multi-Core Processors: Integrates multiples identical cores on a single chip [3].
  Heterogeneous Multi-Core Processors: A complex superscalar core handles general purpose computation.

## Slide 3: Motivation
Advantages: Task isolation and mututal interference [2].
Increasing cores in a process results in:
      Parallel task execution [4].
      Enhances energy efficieny.
      Higher bandwidth [6].
      Lower communication latency [5].
Challenges of scheduling tasks on multicore systems:
      Spatial organization: assigning task to a core.
      Temporal organzation: determining execution order.

## Slide 4: Scheduling multi-core systems
Two fundamental approaches:
  Global Scheduling: Task may execute on any core and migration is allowed.
  Partition-based scheduling: Tasks statically assigned to cores.
Fig. 1: Global Scheduling [7].
Fig. 2: Parition-based scheduling [7].

## Slide 5: Semi-partitioned Scheduling
Partitioning can lead to resource under-utilization: Bin packing problem [7].
Semi-partitioned scheduling is proposed: Tasks statically assigned to fixed cores.
Two parts of semi-partitioned schedulging algorithm:
      Partitioning algorithm: Determines how to split and assign each task to a fixed processor.
      Scheduling Algorithm: Determines how to schedule tasks assigned to each processor.
Communication tasks are grouped in a cluster.
Advantages:
      Minimizes communication costs.
      Balances load across cores.
      Improves system feasiblity.

## Slide 6: Proposed strategy
Partitioning algorithm: Clustering-based.
Scheduling algorithm: Earliest Deadline First (EDF).
Each core must pass the total utilization test:
      ≤ 1
Communication cost depends on relative distance distance between cores.
Goal: Reduced Communication Cost between cores.

## Slide 7: Mathematical Approach
Each core must pass utilization test:
        = ∑ = ∑ ≤ 1
N
i = 1
N
i = 1
Communication cost between core and :
Cost of transferring one byte fromm core to :
Total communication cost is multiplied by volume of exchanged data.

## Slide 8: Implementation and Example
Algorithm: Assign Clusters to Cores
1: for each cluster in clusters do
2: Find the least-loaded core that can still take the cluster‘s total utilization.
3: Assign all tasks in the cluster to that core.
4: Update the core‘s utilization.
5: end for

## Slide 9: Implementation and Example
Task Number | Execution Time | Period
0 | 1 | 5
1 | 2 | 10
2 | 1 | 4
3 | 2 | 8
4 | 3 | 4
5 | 1 | 10
6 | 5 | 6
Table 1: Task Parameters

## Slide 10: Implementation and Example
 | T0 | T1 | T2 | T3 | T4 | T5 | T6
T0 | 0 | 5 | 3 | 9 | 0 | 0 | 0
T1 | 5 | 0 | 4 | 7 | 0 | 0 | 0
T2 | 3 | 4 | 0 | 0 | 0 | 0 | 0
T3 | 9 | 7 | 0 | 0 | 0 | 8 | 0
T4 | 0 | 0 | 0 | 0 | 0 | 0 | 7
T5 | 0 | 0 | 0 | 8 | 0 | 0 | 0
T6 | 0 | 0 | 0 | 0 | 7 | 0 | 0
Table 2: Task dependency matrix

## Slide 11: Implementation and Example
Fig. 4: Task dependency matrix

## Slide 12: Implementation and Example

## Slide 13: Overview and Conclusion
Partition-based scheduling is explored.
Allocation of periodic tasks on homogeneous multi-core architecture is discussed.
Semi-partition scheduling is decided upon.
Implementation in C withFreeRTOS (Repository).
Simulation illustrated in UPPAAL.
Tasks with frequent communication formed cluster.
Clusters allocated on nearby cores, with schedulability constraints.
Communication cost reduced.

## Slide 14: References
[1] Juan Zamorano and Juan Antonio de la Puente. “On real-time partitioned multicore systems”. In: ACM SIGAda Ada Letters 33 (Nov. 2013), pp. 33–39. DOI: 10.1145/2552999.2553003.
[2] C Buttazzo. Hard Real-time Computing Systems: Predictable Scheduling Algorithms and Applications. Springer, 2011.
[3] Yang Pan et al. “The research of multi-core parallel technology”. In: 2012 8th International Conference on Natural Computation. 2012, pp. 1056–1059. DOI: 10. 1109/ICNC.2012.6234619.
[4] L. Hammond et al. “Stanford Hydra CMP”. In: Micro, IEEE 20 (Apr. 2000), pp. 71 –84. DOI: 10. 1109/ 40 . 848474.
[5] Xiuzhen Lian et al. “Cache Coherence Protocols in Shared-Memory Multiprocessors”. In: Jan. 2015. DOI: 10.2991/iccse- 15.2015.52.
[6] M.B. Taylor et al. “The Raw microprocessor: a compu- tational fabric for software circuits and general-purpose programs”. In: IEEE Micro 22.2 (2002), pp. 25–35. DOI: 10.1109/MM.2002.997877.
[7] Hayfa Ben Abdallah, Hamza Gharsellaoui, and Sadok Bouamama. “A Novel Partitioning Approach for Real- Time Scheduling of Mixed-Criticality Systems”. In: Proceedings of the 16th International Conference on Agents and Artificial Intelligence, ICAART 2024, Vol- ume 3, Rome, Italy, February 24-26, 2024. Ed. by Ana Paula Rocha 0001, Luc Steels, and H. Jaap van den Herik. SCITEPRESS, 2024, pp. 882–889. ISBN: 978-989-758-680-4. DOI: 10.5220/0012411200003636. URL: https://doi.org/10.5220/0012411200003636.