## Slide 1: Low Power Scheduling For High Level Synthesis
Hardware Software Co-Design

## Slide 2: Motivation
Key drivers of digital chip design: area, performance and power.
Increasing demand for personal computing devices.
Hence increasing demand for low-power.
Challenges in traditional approach design:
      Time consuming
      Unreliable.
Power issues must be addressed early in design cycle (system level) [1].

## Slide 3: Motivation
Power consumption can be reduced by:
  Reducing chip and package capacitance  Expensive.
  Scaling the supply voltage  Need extra circuits.
  Better design techniques  Cost-effective.
  Power management strategies  significant power savings.
Solution: Integrate power scheduler in High Level Synthesis (HLS) [1].

## Slide 4: Background
High Level Synthesis: Translation function from behavioural to structural description [3].
Required behaviour -> Structure that implements the behaviour.
HLS consists of three phases [1]:
      Scheduling: which clock cycle?
      Allocation: how many resources?
      Binding: which operation to which resource?
Fig. 1: HLS Design Flow [1]

## Slide 5: Background
Short-circuit power dissipation accounts for less than 20% of total dynamic power [1].
Focus: Capacitive switching.
Fig. 2: Sources of power dissipation

## Slide 6: Background
Power Reduction Methods
Fig. 3: Gate clock [1]
Fig. 4: Guarded evaluation [1]
Fig. 5: Power down [1]

## Slide 7: Strategy
Goal 1: Dedicated turn-on and turn-off mechanisms.
Goal 2: Minimizing control components for those mechanisms.
Technique: Clock gating, power down or write enables for guard.
Exploitation of idleness of device.
Integration of low power method in scheduling process.

## Slide 8: Background
Power Scheduler: alternative scheduling technique for power reduction.
Path-based scheduling technique.
Fig. 6: Integration of Power scheduler in HLS design flow. [1]
Fig. 7: Input and output of Power Scheduler [1].

## Slide 9: Background
Fig. 8: Steps of Power Scheduler [1].

## Slide 10: Mathematical Implementation
Total Dynamic power of all nodes:
Dynamic power for a partition:
Total dynamic power dissipation (with control unit):
Power Delay of a partition (with run-time):
Total power delay:

## Slide 11: Fork-Join path calculation
* : two timesteps, + : 1 timestep.
= {*cm2, + , +}, time() = 4
= {*cmo}, time() = 2
= {*cm1,+,*cs}, time() = 5
Fig. 9: Fork-join path analysis [2].

## Slide 12: Control path calculation
* : two timesteps, + : 1 timestep.
= {+ , +}, time() = 2
= {*cmo}, time() = 2
= {*cm1,+,*cs}, time() = 4
Fig. 10: Control path analysis [2].

## Slide 13: Implementation
Partitions:
Fig. 11: Mpeg-2 algorithm example to determine partitions [1].

## Slide 14: Overview and Conclusion
Low power driven synthesis is discussed.
A developed power scheduler is the focus.
Scheduler produces partitioned CDFG.
Partition allows for dedicated turn-on and turn-off mechanism.
Part of MPEG-2 algorithm is used as an example.
Energy saving of 15% achieved [4].

## Slide 15: References
[1] Achim Rettberg, Bernd Kleinjohann, and Franz Rammig. “Low Power Driven High-Level Synthesis for Dedicated Architectures”. In: (Jan. 2006).
[2] Achim Rettberg and Franz Rammig. “Integration of Energy Reduction into High-Level Synthesis by Parti- tioning”. In: From Model-Driven Design to Resource Management for Distributed Embedded Systems. Ed. by Bernd Kleinjohann et al. Boston, MA: Springer US, 2006, pp. 225–234. ISBN: 978-0-387-39362-9.
[3] M.C. McFarland, A.C. Parker, and R. Camposano. “The high-level synthesis of digital systems”. In: Proceedings of the IEEE 78.2 (1990), pp. 301–318. DOI: 10.1109/5. 52214.
[4] A. Rettberg and F.J. Rammig. “A new design partitioning approach for low power high-level synthesis”. In: Third IEEE International Workshop on Electronic Design, Test and Applications (DELTA’06). 2006, 6 pp.–148. DOI: 10. 1109/DELTA.2006.8.